CANSee
2019.01.12
Technical Documentation
# Hardware
## List of components
- 1x ODB case with connector
  https://www.aliexpress.com/item/CASE-ELM327-OBD2-Connector-J1962m-Plug-with-Enclosure-16pin-Male-Connector/32827624441.html
- 1x DOIT ESP32 DEVKIT or similar
  https://www.aliexpress.com/item/ESP32S-ESP-32S-ESP32-ESP-32-CP2102-Wireless-WiFi-Bluetooth-Development-Board-Micro-USB-Dual-Core/32842731763.html
- 1x Mini DC-DC converter
  https://www.aliexpress.com/item/10Pcs-Mini-DC-DC-12-24V-To-5V-3A-Step-Down-Power-Supply-1-8V-2/32848669016.html
- 2x SN65HVD230 CAN bus transceiver
  https://www.aliexpress.com/item/SN65HVD230-CAN-Bus-Transceiver-Communication-Module-Thermal-Protection-Slope-Control-for-Arduino/32851150816.html
- 5x 3mm LED (blue, green, red, yellow, white)
- 4x 120 Ω resistor
- 1x 3.3 kΩ resistor
## Connecting things together
The DC-DC converter must be adjusted to an output of 5V. Don’t mix up CAN connections on the ODB2 connector, as you may break your car’s bus system if improperly connected!
## Pin usage
Pin	Connection
4	RX of main CAN bus
5	TX of main CAN bus
18	RX of multimedia CAN bus
19	TX of multimedia CAN bus
25	blue LED
26	white LED
27	yellow LED
32	red LED
33	green LED

# Software
## The repository
The repository of the CANSee code if located on Gitlab
https://gitlab.com/jeroenmeijer/cansee
## Configuration settings
%
## Serial configuration commands
Command	Explanation
a	Show all buffered free CAN_frames
z	Reboot (needed for all configuration changes except debug mode)
r	Reset configuration to default and reboot.
gxxx	Get free frame with id xxx
ixxx,yyyy	Get ISO-TP frame with id xxx, PID yyyy
nxxx,config	set EEPROM configuration / xxx is determined by this table / 100 Set the flags configuration as hex as ssbbwwlldd [01010200ff] / ss: Serial over USB / 00 for off, any other for on / bb: Bluetooth / 00 for off, any other for on / ww: WiFi / 00 for off, 01 for Station mode, 02 for Soft Access Point mode. For station mode a DHCP server is assumed. / ll: Use leds / 00 for off, ff for on / dd: Debug / 00 for off, ff for on. A bit pattern can be used and added / 01: show CANbus receive free CAN_frame_std 02: show CANbus receive ISO-TP CAN_frame_std 04: show Commands issued 08: show free frame Commands 10: show ISO-TP Commands / 200 Set the Bluetooth name [CANSee] / 201 Set the Bluetooth pin [1234, not implemented by the API!!] / 300 Set the WiFi ssid for Soft Access Point mode [CANSee] / 301 Set the WiFi password for Soft Access Point mode [CANSeeMe] / 400 Set the WiFi ssid for Station mode [Home] / 401 Set the WiFi password for Station mode [Password] / 500 Set CANbus parameter for CAN0 in hex as sprxtx / sp: speed in 25 kbps increments. [0x14 for can0, 0x0a for can1] rx: Rx pin of transceiver [4 for can0, 0x12 for can1] tx: Tx pin of transceiver [5 for can0, 0x13 for can1] Note that this is a very advanced setting and selecting pins that are internally used on your board (notably 6-11) will crash the board. Also pins 34 and up are input only. / 501 Set CANbus parameter for CAN1 in hex as sprxtx (see above). / Usage of the semi-secondary CAN bus by switching the single controller to another pin pair is not supported and basically fails spectacularly.