CANSee
2019.01.12
Technical Documentation
# Hardware
%
## List of components
%
## Connecting things together
%
## Pin usage
%
# Software
%
## The repository
%
## Configuration settings
%
## Serial configuration commands
Command	Explanation
a	Show all buffered free CAN_frames
z	Reboot (needed for all configuration changes except debug mode)
r	Reset configuration to default and reboot.
gxxx	Get free frame with id xxx
ixxx,yyyy	et ISO-TP frame with id xxx, PID yyyy
nxxx,config	set EEPROM configuration

xxx config
=== =======================================================================
100 Set the flags configuration as hex as ssbbwwlldd (01010200ff)
     ss: Serial over USB
       00 for off, any other for on
     bb: Bluetooth
       00 for off, any other for on
     ww: WiFi
       00 for off, 01 for Station mode, 02 for Soft Access Point mode
       For station mode a DHCP server is assumed
     ll: Use leds
       00 for off, ff for on
     dd: Debug
       00 for off, ff for on. A bit pattern can be used and added
        01: show CANbus receive free CAN_frame_std
        02: show CANbus receive ISO-TP CAN_frame_std
        04: show Commands issued
        08: show free frame Commands
        10: show ISO-TP Commands
200 Set the Bluetooth name (CANSee)
201 Set the Bluetooth pin (1234, not implemented by the API!!)
300 Set the WiFi ssid for Soft Access Point mode (CANSee)
301 Set the WiFi password for Soft Access Point mode (CANSeeMe)
400 Set the WiFi ssid for Station mode (Home)
401 Set the WiFi password for Station mode (Password)
500 Set CANbus parameter for can0 in hex as sprxtx
     sp: speed in 25 kbps increments. (0x14 for can0, 0x0a for can1)
     rx: Rx pin of transceiver (4 for can0, 0x12 for can1)
     tx: Tx pin of transceiver (5 for can0, 0x13 for can1)
     Note that this is a very advanced setting and selecting pins that are
     internally used on your board (notably 6-11) will crash the board. Also
     pins 34 and up are input only.
501 Set CANbus parameter for can1 in hex as sprxtx (see above).
     Usage of the semi-secondary CANbus by switching the single controller to
     another pin pair is not supported and basically fails spectacularly.